## Slide 1: Presentation on a research paper titled
A research paper by
Bolin Zhango and Changyong Li
Optimization of RRT-APF based Path Planning

## Slide 2: Introduction
Path planning is essential for autonomous systems navigating complex and dynamic environments such as dense forests or a traffic infested road
Rapidly- exploring Random Tree(RRT) is widely used in high dimensional spaces but suffers from certain conditions
Artificial Potential Field(APF) is widely preferred in collision avoidance and formation control for swarm but fails for a multi agent planning
This research introduces a hybrid of RRT and APF method to improve planning and to negate the shortcomings of the above.

## Slide 3: Rapidly-exploring Random Tree
A sampling-based algorithm used for Path planning in High-dimensional spaces.
Constructs a tree by adding sampling points from space and connecting the nearest node of existing tree.
Can efficiently explore towards goal regions.
Works in complex and/or large spaces.
Not suitable for multi-agent planning.
Lacks in distributed decision-making.
Requires heavy post processing.

## Slide 4: Artificial Potential Field
Motion planning strategy that models robot as a particle in a force field.
The goal attracts the robot whereas the obstacles exert repulsion.
Requires minimal computation and works better in known environments.
Smooth curved paths with fine adjustments.
Robot may get stuck at zones like in between obstacles(i.e., narrow road).
Not ideal for global planning.

## Slide 5: Hybrid APF and RRT for path planning
Combined RRT and APF for guided expansion(i.e., attraction and repulsion forces)
Step size changes based on proximity to obstacles.
Dynamic Weight tuning to avoid sudden changes and escape narrow obstacles
Path smoothing & Optimization

## Slide 6: Flowchart
Initialization
Random point generation
Dynamic Step-size Calculation
Force calculation
Node Generation
Goal Check
Path optimization
End

## Slide 7: Simulation
Tool used: MATLAB R2019a
Number of experiments: 15 per scenario
2D Simulation:
      Grid size: 1000*1000(mms)
      Obstacles: Rectangles and circles
      Scenarios: 4 simple and 10 complex
3D Simulation:
      Grid size: 1000*1000*1000 (mms)
      Obstacles: cuboids, cylinders and spheres
      Scenarios: 3 simple and 12 complex
Metrics monitored:
      Path length
      Search time
      Obstacle avoidance
      Path smoothness

## Slide 8
Settings:
Parameters | Values ( mms)
Initial Step Length | 40
Max iterations | 5000
Goal threshold | 40
Attractive and Repulsive coefficients | 1.0 & 100
Obstacle buffer zone | 40

## Slide 9: Results:
Environment | Metrics | RRT | RRT-APF
Simple | 2D path length | 1882.88 mm | 1857.15 mm
 | 2D Search time | 3.60 s | 1.57 s
 | 3D path length | 2472.02 mm | 1855.79 mm
 | 3D Search time | 3.86 s | 3.22 s
Complex | 2D Path length | 1588.22 mm | 1834.35 mm
 | 2D Search time | 3.58 s | 3.14 s
 | 3D Path length | 2533.39 mm | 1975.21 mm
 | 3D Search time | 7.09 s | 6.09 s

## Slide 10: Conclusion:
RRT-APF algorithm significantly improves individual RRT’s and APF’s limitations
Generates smoother shorter and collisions-free paths
Dynamic step-size and force-weight tuning enhances performance
Useful for real-time robotics in dynamic, complex environments
Improves swarm’s safety and resource efficiency.