## Slide 1
Title: Formation Control for Multiple Unmanned Aerial Vehicles in Constrained Space Using Modified Artificial Potential Field
Authors: Hang Yin, Léa L. Cam, Utpal Roy
Published in: Mathematical Modelling of Engineering Problems, Vol. 4, No. 2, June 2017

## Slide 2
1. Introduction
Formation control of UAVs (Unmanned Aerial Vehicles) is a crucial topic in multi-agent systems, with applications ranging from forest fire monitoring to radar deception. The Artificial Potential Field (APF) method is a well-known approach for path planning and collision avoidance. However, the standard Formation Potential Field (FPF) approach faces limitations like discontinuities and failure in poorly distributed agent scenarios.

## Slide 3
2. Objective
This paper introduces a Modified Artificial Potential Field (MAPF) technique to improve formation tracking and collision avoidance of UAVs in constrained environments. The MAPF addresses the drawbacks of FPF and ensures stable, collision-free formation control.

## Slide 4
3. Problem Statement
The task involves:
Planning and generating a desired formation from random UAV positions.
Maintaining the formation while moving as a group.
Avoiding both inter-UAV and environmental collisions.
Assumptions:
UAVs can estimate global positions.
Communication is possible between all UAVs.
Formation is considered fixed if relative positions remain constant over time.

## Slide 5
4. Proposed Method: Modified Artificial Potential Field (MAPF)
Phases of MAPF
Phase 1: UAVs converge around the formation center using global attractive and local repulsive potential fields.
Phase 2: UAVs move to their designated positions using local attractive and local repulsive fields to maintain formation and avoid collisions.
Potential Fields Used
Global Attractive Field: Pulls UAVs toward the formation center.
Local Attractive Field: Pulls UAVs to target positions.
Local Repulsive Field: Prevents UAVs from colliding.
Constraint Repulsive Field: Prevents collisions with obstacles using a Dirac delta function to model spatial constraints.
Controller Design
A distributed controller calculates forces based on the gradients of potential fields and adjusts UAV motion. A virtual leader's trajectory is dynamically updated to navigate around obstacles.

## Slide 6
5. Simulation Study
Setup: 4 UAVs start at random positions and aim to form a rectangle.
FPF Results: FPF fails when UAVs are unevenly distributed; UAVs can get stuck due to field discontinuities.
MAPF Results: Successfully guides UAVs into position, avoiding collisions and maintaining formation, even with poor initial distribution.

## Slide 7
6. Key Contributions
Introduced a two-phase MAPF-based formation strategy.
Ensured distributed collision avoidance in constrained environments.
Improved field smoothness and removed local minima problems seen in FPF.
Demonstrated effectiveness through 2D simulations.

## Slide 8
7. Conclusions
The MAPF method offers a practical and decentralized solution for UAV formation control in complex environments. It enables UAVs to form and maintain formations autonomously, handling obstacle avoidance without the need for high computational resources.